Gen-Aer Diffused Aeration System

**There are many advantages our system has versus traditional aeration techniques.  It starts with the specially made aeration tubing.  The tubing is made of recycled rubber and has a pore size of 50 microns or less.  This is what enables us to produce the high amount of oxygen with this system.  By simply blowing air thru the tube, we create billions of small bubbles that expand as they rise to the surface, thus giving us high oxygen levels.  We can generate up to 12 lb’s of oxygen/hp/hr.

**Every unit is built specifically for the job at hand.  We do this so we can place the grid of tubing as close to the bottom of the lagoon as possible.  This allows us to get the same amount of oxygen on the bottom of the lagoon that is on top.  By doing this, it helps with bacteria growth and sludge removal.

**Another advantage is that there are no moving parts to our system.  Which means less maintenance/repair cost for the customer.  By using a shroud built on top of the unit, the oxygenated water is forced out across the lagoon as it rises from the grid of aeration tubing.

**Economical savings is another big advantage our system has.  We can take a 16’ Gen-Aer aerator with a 4hp regenerative blower and replace a 10hp paddlewheel.  Generally we tell our customers that the electrical savings(50-75%) alone will pay for the system in less than 2 yrs., not to mention a more efficient aerator.

Please take the time to browse thru the pictures and videos, and feel free to call should you have any questions regarding the enclosed information.

Sincerely,

Tony Heimer

C & H Systems, LLC

Brandon, MS

601-331-4216